## Slide 1: 2. The von neumann model
Rocky K. C. Chang, 12 September 2017
Version 0.1

## Slide 2: Goals of this lecture
Understand the concept of stored program.
Understand the main components in the von Newmann model and their interrelationship.
Understand how high-level program fragment can be represented in instruction sets.
Understand how instructions are executed by the CPU.

## Slide 3: Below Your Program
Application software
  Written in high-level language (HLL)
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers

## Slide 4: From C programs to execution
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Source: Slides by K. Asanovic & V. Stojanovic for CS61C at UC/Berlekey

## Slide 5: From C programs to execution
Compiler: Source code  assembly language (may be skipped)  machine code
Assembler: Assembly code  machine code
Machine code consists of instructions understood by the CPU
Each instruction is executed by CPU
  Data processing (arithmetic, logic)
  Data storage
  Data movement
  Control/management

## Slide 6: An example
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111

## Slide 7: The Stored Program Computer
1943: ENIAC
  Presper Eckert and John Mauchly -- first general electronic computer.
  Hard-wired program -- settings of dials and switches.
1944: Beginnings of EDVAC
  Among other improvements, includes program stored in memory
1945: John von Neumann
  wrote a report on the stored program concept, known as the First Draft of a Report on EDVAC
The basic structure proposed in the draft became known as the “von Neumann machine” (or model).
  a memory, containing instructions and data
  a processing unit, for performing arithmetic and logical operations
  a control unit, for interpreting instructions

## Slide 8: Stored-Program Computer
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
  Source: David Patterson and John Hennessy, Computer Organization and Design, 5th edition, Morgan Kaufman, 2014.

## Slide 9: Everything is now addressable
Since all instructions and data are stored in memory, everything has a memory address: instructions, data words
  both branches and jumps use these
C pointers are just memory addresses: they can point to anything in memory
  Unconstrained use of addresses can lead to nasty bugs; up to you in C; limited in Java by language design
One register keeps address of instruction being executed: Program Counter (PC)

## Slide 10: instructions
The instruction is the fundamental unit of work.
Specifies two things:
  opcode: operation to be performed
  operands: data/locations to be used for operation
An instruction is encoded as a sequence of bits (Just like data!)
  Often, but not always, instructions have a fixed length, such as 16 or 32 bits.
  Control unit interprets instruction: generates sequence of control signals to carry out operation.
  Operation is either executed completely, or not at all.
A computer’s instructions and their formats is known as its Instruction Set Architecture (ISA).
Opcode

## Slide 11: Example: Add instruction
Each instruction is 16 bit long and has a four-bit opcode, bits [15:12].
Eight registers (R0-R7) for temporary storage.
ADD instruction: Sources and destination of ADD are registers.
  Data are assumed loaded into registers Src1 and Src2.
“Add the contents of R2 to the contents of R6, and store the result in R6.”

## Slide 12: Example: LOAD (LDR) Instruction
Load (LDR) instruction -- read data from memory
Base + offset mode:
  Add offset to base register -- result is memory address
  Load from memory address into destination register
“Add the value 6 to the contents of R3 to form a memory address. Load the contents stored in that address to R2.”

## Slide 13: Example: STORE (STR) Instruction
Store (STR) instruction -- store data to memory
Base + offset mode:
  Add offset to base register -- result is memory address
  Store data from the source register to the memory address
“Add the value 6 to the contents of R3 to form a memory address. Store the contents in R2 to that address.”
STR
0 1 1 1
SR

## Slide 14: The von Neumann model

## Slide 15: Flow of Information
The parts are connected to one another by a collection of wires called a bus.

## Slide 16: The three elements
Memory: Store and retrieve instructions and data.
Processor: Houses two separate components:
  The control unit: repeating the three tasks:
    Fetch an instruction from memory
    Decode the instruction
    Execute the instruction
  The arithmetic/logic unit (ALU): Perform mathematical and logical operations.
Input/Output (I/O) Units: Handle communication with the outside world.
  Source: M. Schneider and J. Gersting, Invitation to Computer Science, 5th edition, Course Technology, 2010.

## Slide 17: Memory Subsystem
Memory, also called RAM (Random Access Memory)
  Consist of many memory cells (storage units) of a fixed size. Each cell has an address associated with it: 0, 1, …
  All accesses to memory are to a specified address. A cell is the minimum unit of access (fetch/store a complete cell).
  The time it takes to fetch/store a cell is the same for all cells.
When the computer is running, both
  Program
  Data (variables)
are stored in the memory.

## Slide 18: RAM
Need to distinguish between
  the address of a memory cell and the content of a memory cell
Memory width (W):
  How many bits is each memory cell, typically one byte (=8 bits)
Address width (N):
  How many bits used to represent each address, determines the maximum memory size = address space.
  If address width is N-bits, then address space is 2N (0,1,...,2N-1).
...
0
1
2
2N-1
1 bit
W
0000000000000001
N
2N

## Slide 19: Memory Size / Speed
Memory sizes:
  Kilobyte (KB) = 210 = 1,024 bytes ~ 1 thousand
  Megabyte(MB) = 220 = 1,048,576 bytes ~ 1 million (106) bits
  Gigabyte (GB) = 230 = 1,073,741,824 bytes ~ 1 billion (109) bits
  Terabyte (TB) = 240 = …
Memory Access Time (read from/ write to memory)
  50-75 nanoseconds (1 nsec. = 0.000000001 sec.)
RAM is
  volatile (can only store when power is on)
  relatively expensive

## Slide 20: Operations on Memory
Fetch (address):
  Fetch a copy of the content of memory cell with the specified address.
  Non-destructive, copies value in memory cell.
Store (address, value):
  Store the specified value into the memory cell specified by address.
  Destructive, overwrites the previous value of the memory cell.
The memory system is interfaced via:
  Memory Address Register (MAR)
  Memory Data Register (MDR)
  Fetch/Store signal

## Slide 21: Structure of the Memory Subsystem
Fetch (address)
  Load address into MAR.
  Decode the address in MAR.
  Copy the content of memory cell with specified address into MDR.
Store (address, value)
  Load the address into MAR.
  Load the value into MDR.
  Decode the address in MAR
  Copy the content of MDR into memory cell with the specified address.
MAR
MDR
...
Memory
decoder
circuit
Fetch/Store
controller
F/S

## Slide 22: Review questions
If memory address is of n bits, and each computer word stored in the memory is of 32 bits, how many words can be stored in the memory?
If each computer word is of 64 bits and the memory is designed to accommodate 2m words, how many bits are needed for the memory addresses?
How much memory can be addressed by a 32/64-bit machine?

## Slide 23: Input/Output Subsystem
Handles devices that allow the computer system to:
  Communicate and interact with the outside world
    Screen, keyboard, printer, ...
  Store information (mass-storage)
    Hard-drives, floppies, CD, tapes, …
Mass-Storage Device Access Methods:
  Direct Access Storage Devices (DASDs)
    Hard-drives, floppy-disks, CD-ROMs, ...
  Sequential Access Storage Devices (SASDs)
    Tapes (for example, used as backup devices)

## Slide 24: I/O Controllers
Speed of I/O devices is slow compared to RAM
  RAM ~ 50 nsec.
  Hard-Drive ~ 10msec. = (10,000,000 nsec)
Solution:
  I/O Controller, a special purpose processor:
    Has a small memory buffer, and a control logic to control I/O device (e.g. move disk arm).
    Sends an interrupt signal to CPU when done read/write.
  Data transferred between RAM and memory buffer.
  Processor free to do something else while I/O controller reads/writes data from/to device into I/O buffer.

## Slide 25: Structure of the I/O Subsystem
I/O controller
I/O Buffer
Control/Logic
I/O device
Data from/to memory
Interrupt signal (to processor)

## Slide 26: The ALU Subsystem
The ALU (Arithmetic/Logic Unit) performs
  mathematical operations (+, -, x, /, …)
  logic operations (=, <, >, and, or, not, ...)
In today's computers integrated into the CPU
Consists of:
  Circuits to do the arithmetic/logic operations.
  Registers (fast storage units) to store intermediate computational results.
  Bus that connects the two.

## Slide 27: Structure of the ALU
Registers:
  Very fast local memory cells, that store operands of operations and intermediate results.
  CCR (condition code register), a special purpose register that stores the result of <, = , > operations
ALU circuitry:
  Contain an array of circuits to do mathematical/logic operations.
Bus:
  Data path interconnecting the registers to the ALU circuitry.
ALU circuitry
GT
EQ
LT
R0
R1
R2
Rn

## Slide 28: The Control Unit
Program is stored in memory
  as machine language instructions, in binary
The task of the control unit is to execute programs by repeatedly:
  Fetch from memory the next instruction to be executed.
  Decode it, that is, determine what is to be done.
  Execute it by issuing the appropriate signals to the ALU, memory, and I/O subsystems.
  Continue until the HALT instruction

## Slide 29: The fetch-decode-execute cycle

## Slide 30: Structure of the Control Unit
PC (Program Counter):
  store the address of next instruction to fetch
IR (Instruction Register):
  store the instruction fetched from memory
Instruction Decoder:
  Decode instruction and activates necessary circuitry
Instruction
Decoder
IR
+1
PC

## Slide 31: A simple example
c  a + b (using a HLL)
The compiler will compile it into 4 instructions:
  Load a into register R1 (LDR R1, 1000)
  Load b into register R3 (LDR R3, 1002)
  R2  R1 + R2 (ADD R2, R1, R2)
  Store R2 to c. (STR R2, 1003)
  And store their corresponding machine codes in the memory.

## Slide 32: A simple example
1000 (a)
1002 (b)
1004 (c)
10
20
-100
5000
5002
5004
LDR R1, 1000
5006
LDR R3, 1002
ADD R2, R1, R3
STR R2, 1004
ALU
R0
R1
R2
R3
IR
PC
5000
LDR R1, 1000
10

## Slide 33: A simple example
1000 (a)
1002 (b)
1004 (c)
10
20
-100
5000
5002
5004
LDR R1, 1000
5006
LDR R3, 1002
ADD R2, R1, R3
STR R2, 1004
ALU
R0
R1
R2
R3
IR
PC
5002
LDR R3, 1002
10
20

## Slide 34: A simple example
1000 (a)
1002 (b)
1004 (c)
10
20
-100
5000
5002
5004
LDR R1, 1000
5006
LDR R3, 1002
ADD R2, R1, R3
STR R2, 1004
ALU
R0
R1
R2
R3
IR
PC
5004
10
20
ADD R2, R1, R3
30

## Slide 35: A simple example
1000 (a)
1002 (b)
1004 (c)
10
20
-100
5000
5002
5004
LDR R1, 1000
5006
LDR R3, 1002
ADD R2, R1, R3
STR R2, 1004
ALU
R0
R1
R2
R3
IR
PC
5006
10
20
30
STR R2, 1004
30

## Slide 36: Review questions
Write down the instructions for d  (a + b) × c, assuming a, b, and c are integers.

## Slide 37: Instruction Processing
Decode instruction
Evaluate address
Fetch operands from memory
Execute operation
Store result
Fetch instruction from memory

## Slide 38: Instruction Processing: FETCH
Load next instruction (at address stored in PC) from memory into Instruction Register (IR).
  Load contents of PC into MAR.
  Send “read” signal to memory.
  Read contents of MDR, store in IR.
Then increment PC, so that it points to the next instruction in sequence.
  PC becomes PC+1.
EA
OP
EX
S
F
D

## Slide 39: Instruction Processing: DECODE
First identify the opcode.
  E.g., in the first four bits of instruction.
  A 4-to-16 decoder asserts a control line corresponding to the desired opcode.
Depending on opcode, identify other operands from the remaining bits.
  Example:
    for LDR, last six bits is offset
    for ADD, last three bits is source operand #2
EA
OP
EX
S
F
D

## Slide 40: Instruction Processing: EVALUATE ADDRESS
For instructions that require memory access, compute address used for access.
Examples:
  add offset to base register (as in LDR)
  add offset to PC (or to part of PC)
  add offset to zero
EA
OP
EX
S
F
D

## Slide 41: Instruction Processing: FETCH OPERANDS
Obtain source operands needed to perform operation.
Examples:
  load data from memory (LDR)
  read data from register file (ADD)
EA
OP
EX
S
F
D

## Slide 42: Instruction Processing: EXECUTE
Perform the operation, using the source operands.
Examples:
  send operands to ALU and assert ADD signal
  do nothing (e.g., for loads and stores)
EA
OP
EX
S
F
D

## Slide 43: Instruction Processing: STORE
Write results to destination. (register or memory)
Examples:
  result of ADD is placed in destination register
  result of memory load is placed in destination register
  for store (STR) instruction, data is stored to memory
    write address to MAR, data to MDR
    assert WRITE signal to memory
EA
OP
EX
S
F
D

## Slide 44: Changing the Sequence of Instructions
In the FETCH phase, we incremented the Program Counter by 1.
What if we don’t want to always execute the instruction that follows this one?
  examples: loop, if-then, function call
Need special instructions that change the contents of the PC.
These are called jumps and branches.
  jumps are unconditional -- they always change the PC
  branches are conditional -- they change the PC only if some condition is true (e.g., the contents of a register is zero)

## Slide 45: Example: JUMP (JMPR) Instruction
Set the PC to the value obtained by adding an offset to a register. This becomes the address of the next instruction to fetch.
“Add the value of 6 to the contents of R3, and load the result into the PC.”
Notes: This matches the example in the text, but it may be a little confusing because there is no JMPR in the table in Chapter 5. Instead, there’s a JSRR -- bit 11 determines whether to link or not, which determines whether it’s JMPR or JSRR.

## Slide 46: Instruction Processing Summary
Instructions look just like data -- it’s all interpretation.
Three basic kinds of instructions:
  computational instructions (ADD, AND, …)
  data movement instructions (LD, ST, …)
  control instructions (JMP, BRnz, …)
Six basic phases of instruction processing:
F  D  EA  OP  EX  S
  not all phases are needed by every instruction
  phases may take variable number of machine cycles

## Slide 47: Driving Force: The Clock
The clock is a signal that keeps the control unit moving.
  At each clock “tick,” control unit moves to the next machine cycle -- may be next instruction or next phase of current instruction.
Clock generator circuit:
  Based on crystal oscillator
  Generates regular sequence of “0” and “1” logic levels
  Clock cycle (or machine cycle) -- rising edge to rising edge
“1”
“0”
time
Machine
Cycle

## Slide 48: Stopping the Clock
Control unit will repeat instruction processing sequence as long as clock is running.
  If not processing instructions from your application, then it is processing instructions from the Operating System (OS).
  The OS is a special program that manages processor and other resources.
To stop the computer:
  AND the clock generator signal with ZERO
  when control unit stops seeing the CLOCK signal, it stops processing

## Slide 49: Control unit state diagram
The control unit is a state machine. Here is part of a simplified state diagram for an instruction set:
The fetch phase

## Slide 50: Computer Architecture and organization
Instruction set architecture (from Patterson and Hennessy): An abstract interface between the hardware and the lowest-level software that encompasses all the information necessary to write a machine language program that will run correctly, including instructions, registers, memory access, I/O, and so on.
  E.g., Intel x86 family, ARM, MIPS
Microarchitecture (from Patterson and Hennessy): The organization of the processor, including the major functional units, their interconnection, and control.
  (IEEE/ACM Computer Science Curriculum 2008) The internal implementation of a computer at the register and functional unit level

## Slide 51: Conclusions
Processor
Control
Datapath
51
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Source: Slides by K. Asanovic & V. Stojanovic for CS61C at UC/Berlekey

## Slide 52: Reading
Read 3.1-3.3 in Stallings
(Supplement) Read chapter 5 in M. Schneider and J. Gersting, Invitation to Computer Science, 5th edition, Course Technology, 2010 (available in the Internet).
For your interests:
  Intel, ARM: ‘Von Neuman Architecture’ Here to Stay, For Now, Says Bernstein (http://www.barrons.com/articles/intel-arm-von-neuman-architecture-here-to-stay-for-now-says-bernstein-1465242162)
  Understanding the MAR and the MDR (https://www.cs.umd.edu/class/sum2003/cmsc311/Notes/Overall/mar.html)

## Slide 53: acknowledgements
This set of slides are prepared mainly based on
  Chapter 4 in Y. Patt and S. Patel, Introduction to Computing Systems: From Bits and Gates to C and Beyond, second edition, McGraw Hill, 2004.
  Chapter 5 in M. Schneider and J. Gersting, Invitation to Computer Science, 5th edition, Course Technology, 2010.
  Yngvi Bjornsson, Slides for CMPUT101 Introduction to Computing (Chapter 5.1-5.2).

## Slide 54: End