## Slide 1: 2. Instruction sets I
Rocky K. C. Chang
Version 0.3, 14 September 2017

## Slide 2: Goals of this lecture
Know how to write MIPS assembly language for
  Arithmetic operations
  Logical operations
  Data transfer between registers and memory
  Control flow (branching and loops)
Understand two different types of byte order

## Slide 3: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
3
Logic Circuit Description (Circuit Schematic Diagrams)

## Slide 4: Assembly Language
Basic job of a CPU: execute lots of instructions.
Instructions are the primitive operations that the CPU may execute.
Different CPUs implement different sets of instructions. The set of instructions a particular CPU implements is an Instruction Set Architecture (ISA).
  Examples: ARM, Intel x86, MIPS, RISC-V, IBM/Motorola PowerPC (old Mac), Intel IA64, ...

## Slide 5: Instruction Set Architectures
Early trend was to add more and more instructions to new CPUs to do elaborate operations
  VAX architecture had an instruction to multiply polynomials!
RISC philosophy (Cocke IBM, Patterson, Hennessy, 1980s) – Reduced Instruction Set Computing
  Keep the instruction set small and simple, makes it easier to build fast hardware.
  Let software do complicated operations by composing simpler ones.

## Slide 6: MIPS Architecture
MIPS – semiconductor company that built one of the first commercial RISC architectures
We will study the MIPS architecture in some detail in this class.
Why MIPS instead of Intel x86?
  MIPS is simple, elegant. Don’t want to get bogged down in gritty details.
  MIPS widely used in embedded apps, x86 little used in embedded, and more embedded computers than PCs

## Slide 7: MIPS32 (32-bit instructions)
7
Memory
Bytes
Program
Data
One MIPS Instruction = 32 bits

## Slide 8: How program is executed?
Processor
Control
Datapath
Program Counter
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Bytes
Instruction
Address
Read Instruction Bits
Program
Data
The program counter (internal register inside processor) holds address of next instruction to be executed

## Slide 9: Assembly Variables: Registers
Unlike HLL like C or Java, assembly cannot use variables
  Why not? Keep hardware simple
Assembly operands are registers.
  Limited number of special locations built directly into the hardware
  Operations can only be performed on these registers!
Benefit: Since registers are directly in hardware, they are very fast (faster than 1 ns - light travels 30cm in 1 ns!!! )

## Slide 10: Number of MIPS Registers
Drawback: Since registers are in hardware, there are a predetermined number of them.
  Solution: MIPS code must be very carefully put together to efficiently use registers.
32 registers in MIPS
  Why 32? Smaller is faster, but too small is bad. Goldilocks problem.
Each MIPS register is 32 bits wide
  Groups of 32 bits called a word in MIPS

## Slide 11: Names of MIPS Registers
Registers are numbered from 0 to 31
Each register can be referred to by number or name.
Number references:
  $0, $1, $2, … $30, $31
For now:
  $16 - $23  $s0 - $s7 (correspond to “saved” variables)
  $8 - $15  $t0 - $t7 (correspond to temporary variables)
  Later will explain other 16 register names
In general, use names to make your code more readable

## Slide 12: C, Java variables vs. registers
In C (and most High Level Languages) variables declared first and given a type
  Example: int fahr, celsius; char a, b, c, d, e;
Each variable can ONLY represent a value of the type it was declared as (cannot mix and match int and char variables).
In Assembly Language, registers have no type; operation determines how register contents are treated.

## Slide 13: Addition and subtraction instructions

## Slide 14: Addition and Subtraction of Integers
Addition in Assembly
  Example: add $s0,$s1,$s2 (in MIPS)
  Equivalent to: a = b + c (in C)
  where C variables ⇔ MIPS registers are: a ⇔ $s0, b ⇔ $s1, c ⇔ $s2
Subtraction in Assembly
  Example: sub $s3,$s4,$s5 (in MIPS)
  Equivalent to: d = e - f (in C)
  where C variables ⇔ MIPS registers are: d ⇔ $s3, e ⇔ $s4, f ⇔ $s5

## Slide 15: Addition and Subtraction of Integers (cont’d)
How to translate the following C statement?
a = b + c + d - e;
Break into multiple instructions:
  add $t0, $s1, $s2 # temp = b + c
  add $t0, $t0, $s3 # temp = temp + d
  sub $s0, $t0, $s4 # a = temp - e
A single C statement may break up into several lines of MIPS.
Notice the use of temporary registers – don’t want to modify the saved variable registers $s.
Everything after the hash mark on each line is ignored (comments)

## Slide 16: Immediate operands
Immediates are numerical constants.
They appear often in code, so there are special instructions for them.
  Otherwise, need more instructions to fetch them from the memory.
Add Immediate:
  addi $s0,$s1,-10 (in MIPS)
  f = g - 10 (in C)
  where MIPS registers $s0,$s1 are associated with C variables f, g.
Syntax similar to add instruction, except that last argument is a number instead of a register.
No subtract immediate instruction

## Slide 17: The constant zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 18: Overflow Arithmetic
Recall: Overflow occurs when there is a “mistake” in arithmetic due to the limited precision in computers.
Example (4-bit unsigned numbers):
  15 1111
  + 3 + 0011
  18 10010
But we don’t have room for 5-bit solution, so the solution would be 0010, which is +2, and “wrong”.

## Slide 19: Overflow handling in MIPS
Some languages detect overflow (Ada), some don’t (most C implementations)
MIPS solution is 2 kinds of arithmetic instructions:
  These cause overflow to be detected
    add (add)
    add immediate (addi)
    subtract (sub)
  These do not cause overflow detection
    add unsigned (addu)
    add immediate unsigned (addiu)
    subtract unsigned (subu)
Compiler selects appropriate arithmetic
  MIPS C compilers produce addu, addiu, subu

## Slide 20: Instructions for Data transfer between registers and Memory
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data = Store to memory
Read Data = Load from
memory
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Source: Slides by K. Asanovic & V. Stojanovic for CS61C at UC/Berlekey

## Slide 21: Byte addressing
0
1
2
3
…
Lots of data is smaller than 32 bits, but rarely smaller than 8 bits – works fine if everything is a multiple of 8 bits
8 bit chunk is called a byte (1 word = 4 bytes)
Memory addresses are really in bytes, not words
Word addresses are 4 bytes apart.
  Word address is same as address of leftmost byte.
  Byte order
0
4
8
12
…
1
5
9
13
…
2
6
10
14
…
3
7
11
15
…
Addr of lowest byte in word is addr of word

## Slide 22: Byte Order
Problem: What order do we read numbers (and other data types) that occupy more than one byte?
Example: 12345678hex
  It can be stored in 4 x 8bit locations as follows.
  Address Order (1) Order (2)
  184 12 78
  185 34 56
  186 56 34
  187 78 12
Notes: 27

## Slide 23: Endianness
The problem is called Endianness.
The system on the left (read top down) has the least significant byte in the highest address  This is called Big-endian.
The system on the right (read bottom up) has the least significant byte in the lowest address  This is called Little-endian.
  Little-endian: e.g., Intel 80x86, x86, VAX, Alpha
  Big-endian; e.g., IBM System 370/390, the Motorola 680x0, Sun SPARC, and most RISC machines.
Notes: 29

## Slide 24: Example of C Data Structure
1 word = 4 byte
Source: Stallings, Computer organization and architecture: Designing for performance, 9th edition, Prentice Hall, 2013.

## Slide 25: Alternative View of C Prog. Example
Source: Stallings, Computer organization and architecture: Designing for performance, 9th edition, Prentice Hall, 2013.

## Slide 26: Transfer from Memory to Register
C code
int A[100];
g = h + A[3];
Using Load Word (lw) in MIPS:
lw $t0,12($s3) # Temp reg $t0 gets A[3]
add $s1,$s2,$t0 # g = h + A[3]
Note: $s3 – base register (containing the starting address of A)
12 – offset in bytes
Offset must be a constant known at assembly time.

## Slide 27: Transfer from Register to Memory
C code
int A[100];
A[10] = h + A[3];
Using Store Word (sw) in MIPS:
lw $t0,12($s3) # Temp reg $t0 gets A[3]
add $t0,$s2,$t0 # Temp reg $t0 gets h + A[3]
sw $t0, 40($s3) # A[10] = h + A[3]
Note: $s3 – base register (containing the starting address of A)
12,40 – offsets in bytes
Notes: 80 – 5 (Clicker) – 3 (News/Administrativia) = 72 (36 slides max)
Clicker at 20 (half+)

## Slide 28: Loading and Storing bytes
Transferring a byte between a register and the memory.
  lb (load byte) and sb (store byte)
  Same format as lw, sw
  E.g., lb $s0, 3($s1): load a byte from the memory address of (3 + the content of $s1) to the low byte position of register $s0.
Signed and unsigned load byte
  lbu (unsigned lb): filling in the rest with 0
    E.g., loading 10000001  00000000 00000000 00000000 10000001
    E.g., loading 01000001  00000000 00000000 00000000 01000001
  lb (signed lb): filling in the rest with the sign bit (sign extension)
    E.g., loading 10000001  11111111 11111111 11111111 10000001
    E.g., loading 01000001  00000000 00000000 00000000 01000001

## Slide 29: Speed of Registers vs. Memory
Given that
  Registers: 32 words (128 bytes)
  Memory: Billions of bytes (2 GB to 8 GB on laptop)
and the RISC principle is…
  Smaller is faster
How much faster are registers than memory?
  About 100-500 times faster in terms of latency of one access!

## Slide 30: Review Question
Assume that the base address of array A[] is in $s3, and the value of h is in $s2. Compile the following C statement into MIPS assembly.
A[16] = h + A[8];

## Slide 31: Review Question
  We want to translate *x = *y +1 into MIPS (x, y pointers stored in: $s0 and $s1). Which one is correct?
  A: addi $s0,$s1,1
  B: lw $s0,1($s1)
  sw $s1,0($s0)
  C: lw $t0,0($s1)
  addi $t0,$t0,1
  sw $t0,0($s0)
  D: sw $t0,0($s1)
  addi $t0,$t0,1
  lw $t0,0($s0)
  E: lw $s0,1($t0)
  sw $s1,0($t0)

## Slide 32: Instructions for Logical operations

## Slide 33: MIPS Logical Instructions
Logical operations | C operators | Java operators | MIPS instructions
Bit-by-bit AND | & | & | and
Bit-by-bit OR | ¦ | ¦ | or
Bit-by-bit NOT | ~ | ~ | not
Shift left | << | << | sll
Shift right | >> | >>> | srl
Useful to operate on fields of bits within a word
  e.g., characters within a word (8 bits)
Operations to pack /unpack bits into words
Called logical operations

## Slide 34: Logic Shifting
Shift Left: sll $s1,$s2,2 #s1=s2<<2
  Store in $s1 the value from $s2 shifted 2 bits to the left (they fall off end), inserting 0’s on right
    Before: 0000 0002hex 0000 0000 0000 0000 0000 0000 0000 0010two
  After: 0000 0008hex 0000 0000 0000 0000 0000 0000 0000 1000two
  What arithmetic effect does shift left have?
Shift Right: srl is opposite shift; >>
  What arithmetic effect does shift right have?

## Slide 35: Arithmetic Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contains
  1111 1111 1111 1111 1111 1111 1110 0111two= -25ten
If executed sra $s0, $s0, 4, result is:
1111 1111 1111 1111 1111 1111 1111 1110two= -2ten
  Unfortunately, this is NOT same as dividing by 2n
    Fails for odd negative numbers
    C arithmetic semantics is that division should round towards 0
Notes: \

## Slide 36: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 37: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
$t2
$t1
$t0
0000 0000 0000 0000 0011 1100 0000 0000
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1101 1100 0000

## Slide 38: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
In keeping with the three-operand format, include the instruction NOR (NOT OR) instead of NOT.
  If one operand is zero, it is equivalent to NOT: A NOR 0 = NOT (A OR 0) = NOT (A).
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0

## Slide 39: Review question
Assume the following register contents: $t0 = 0xAAAAAAAA, $t1 = 0x12345678.
For the register values shown above, what is the value of $t2 for the following sequence of instructions?
sll $t2, $t0, 4
andi $t2, $t2, −1

## Slide 40: Instructions for control flow

## Slide 41: Types of Branches
Conditional Branch – change control flow depending on outcome of comparison
  MIPS instructions: branch if equal (beq) or branch if not equal (bne)
beq register1,register2,L1
means: go to statement labeled L1 if (value in register1) == (value in register2)
otherwise, go to the next statement
Unconditional Branch – always branch
  MIPS instruction: jump (j)

## Slide 42: if Statement example
Assuming translations below, compile if block
$s0f $s1g $s2h $s3i $s4j
if (i == j) bne $s3,$s4,Exit
f = g + h; add $s0,$s1,$s2
Exit:
May need to negate branch condition.

## Slide 43: if-else Statement example
Assuming translations below, compile
$s0f $s1g $s2h $s3i $s4j
if (i == j) bne $s3,$s4,Else
f = g + h; add $s0,$s1,$s2
else j Exit
f = g – h; Else: sub $s0,$s1,$s2
Exit:

## Slide 44: Inequalities in MIPS
General programs need to test < and > as well.
MIPS Inequality Instruction:
  “Set on Less Than”
  Syntax: slt reg1, reg2, reg3
  Meaning: if (reg2 < reg3) reg1 = 1; else reg1 = 0;
  “set” means “change to 1”, “reset” means “change to 0”.

## Slide 45: Inequalities in MIPS (Cont’d)
How do we use this? Compile by hand: if (g < h) goto Less; #g:$s0, h:$s1
Answer: compiled MIPS code…
slt $t0,$s0,$s1 # $t0 = 1 if g<h bne $t0,$zero,Less # if $t0!=0 goto Less
Register $zero always contains the value 0, so bne and beq often use it for comparison after an slt instruction.
sltu treats registers as unsigned.

## Slide 46: Immediates in Inequalities
slti an immediate version of slt to test against constants
  Loop: . . . slti $t0,$s0,1 # $t0 = 1 if # $s0<1 beq $t0,$zero,Loop # goto Loop # if $t0==0 # (if ($s0>=1))

## Slide 47: Loops in C/Assembly
Simple loop in C; A[] is an array of int
  do { g = g + A[i]; i = i + j; } while (i != h);
Use this mapping: g, h, i, j, &A[0] $s1, $s2, $s3, $s4, $s5
Loop: sll $t1,$s3,2 # $t1= 4*i addu $t1,$t1,$s5 # $t1=addr A+4i lw $t1,0($t1) # $t1=A[i] add $s1,$s1,$t1 # g=g+A[i] addu $s3,$s3,$s4 # i=i+j bne $s3,$s2,Loop # goto Loop # if i!=h

## Slide 48: Review question
Assume $t0 holds the value 0x00101000. What is the value of $t2 after the following instructions?
slt $t2, $0, $t0
bne $t2, $0, ELSE
j DONE
ELSE: addi $t2, $t2, 2
DONE:

## Slide 49: Review question
Consider the following MIPS loop:
LOOP: slt $t2, $0, $t1
beq $t2, $0, DONE
subi $t1, $t1, 1
addi $s2, $s2, 2
j LOOP
DONE:
Assume that the register $t1 is initialized to the value 10. What is the value in register $s2 assuming $s2 is initially zero?

## Slide 50: Conclusion
Computer words and vocabulary are called instructions and instruction set respectively.
MIPS is example RISC instruction set in this class.
Rigid format: 1 operation, 2 source operands, 1 destination
  add,sub,mul,div,and,or,sll,srl,sra
  lw,sw,lb,sb to move data to/from registers from/to memory
  beq, bne, j, slt, slti for decision/flow control
Simple mappings from arithmetic expressions, array access, if-then-else in C to MIPS instructions

## Slide 51: Reading
Read 2.1-2.7 in David Patterson and John Hennessy, Computer Organization and Design, 5th edition, Morgan Kaufmann, 2014.

## Slide 52: acknowledgements
This set of slides are prepared mainly based on
  The slides prepared by K. Asanovic & V. Stojanovic for CS61C at UC/Berkeley (http://inst.eecs.Berkeley.edu/~cs61c/sp15)

## Slide 53: End