## Slide 1: 7. Building datapath
Rocky K. C. Chang 6 November 2017

## Slide 2: Goals of this lecture
We will implement a subset of MIPS instructions using single clock cycle.
Simple subset, shows most aspects
  Memory reference: lw, sw
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq, j

## Slide 3: Instruction Processing
Decode instruction
Evaluate address
Fetch operands from memory
Execute operation
Store result
Fetch instruction from memory

## Slide 4: Instruction Execution
The first two steps are the same for all instructions:
  PC  instruction memory, fetch instruction
  PC  PC + 4
  Decode the instruction: The operation and operands (register numbers, immediate, target address)
Depending on the instruction class
  Use ALU to calculate
    Arithmetic-logical result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC  target address

## Slide 5: CPU Overview

## Slide 6: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 7: Control

## Slide 8: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
  Refining the overview design

## Slide 9: Instruction Fetching
Program counter
Adder
Instruction memory
Which one(s) is combinational / sequential circuit?
Do they need control signal?
32-bit register
Increment by 4 for next instruction

## Slide 10: R-Format Instructions
E.g., add $s0,$s1,$s2
Read two register operands
Perform arithmetic/logical operation
Write register result
  Controlled by a write control signal

## Slide 11: Load/Store Instructions (I format)
lw/sw $t1, offset_value($t2)
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 12: Branch Instructions (I format) 1/2
beq $t1, $t2, offset
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch

## Slide 13: Branch Instructions 2/2
Just re-routes wires
Sign-bit wire replicated

## Slide 14: Composing the Elements
The data path does an instruction in one clock cycle.
  Each datapath element can only do one function at a time.
  Hence, we need separate instruction and data memories.
Use multiplexers where alternate data sources are used for different instructions.

## Slide 15: R-format/Load/Store Datapath 1/2
Problem: Building a datapath for R-format instructions and load/store instructions.
Their main differences:
  One of the inputs to the ALU is different: a register for R-format instructions and a sign-extended 16-bit offset from the load/store instructions.
  The value stored in the destination register: the ALU for R-format and the memory for the load instruction.
Solution:
  Allow two different sources for the input to the ALU.
  Allow two different sources for the data stored into the register file.

## Slide 16: R-format/Load/Store Datapath 2/2

## Slide 17: Full Datapath for R-format, load/store and branch

## Slide 18: A simple implementation scheme
Implement a subset of MIPS32 using the datapath from the last slide and a control function.
This subset includes
  add, sub, AND, OR, set on less than
  lw, sw, beq, and
  j

## Slide 19: ALU Control (from a Simple ALU) 1/4
The four-bit ALU control: 1-bit Ainvert, 1-bit Binvert and 2-bit Operation
  2-bit Operation: 00 (AND), 01 (OR), 10 (add), 11 (set-on-less-than)
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 20: ALU Control 2/4
AND: R-format
OR: R-format
Add: R-format and load/store
Subtract: R-format and branch equal
Set-on-less-than: R-format
NOR: for other instructions

## Slide 21: ALU Control 3/4
Design a combinational logic circuit for generating the 4-bit ALU control bits
  Input: 2-bit ALUOp (derived from opcode) and the 6-bit function field in R-format instructions.
opcode | ALUOp | Operation | Funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | Add | 100000 | add | 0010
 |  | Subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111

## Slide 22: ALU control 4/4
ALU control
Main control
Funct field for R-format instructions
2-bit ALUOp
Opcode

## Slide 23: Review question
Design the combinational circuit for the ALU control unit on slide 21.

## Slide 24: Other seven control signals

## Slide 25: Instruction decoding
Identify the fields of an instruction and the control lines needed for slide 17.
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-format and load
sign-extend and add

## Slide 26: Instruction decoding
op[5:0]: inputs to the main control unit for generating control signals for all instructions
rs[25:21] and rt[20:16]: registers to be read for the R-format instructions, branch equal, and store.
rs[25:21]: base register for load and store instructions.
The destination register: rt[20:16] for load and rd[15:11] for R-format instructions.
  Need a multiplexer to select between the two.
funct[5:0]: inputs to the ALU control

## Slide 28: Data path for R-format instructions
For example, add $t1,$t2,$t3.
Three steps:
  The instruction fetched and the PC incremented
  Two registers, $t2 and $t3, read from the register file; the main control unit computes the setting of the control lines.
  The ALU operates on the data read from the register file, using the function code to generate the ALU function.
These steps will be completed in one clock cycle.

## Slide 29
Which control lines should be active?

## Slide 30: Data path for load instruction
For example, lw $t1, offset($t2)
Five steps:
  An instruction fetched and the PC incremented
  A register ($t2) value read from the register file
  The ALU computes the sum of the value read from the register file and the sign-extended, lower 16 bits of the instruction.
  The sum from the ALU is used as the address for the data memory.
  The data from the memory unit is written into the register file; the register destination is given by bits 20:16 of the instruction ($t1).

## Slide 31
Which control lines should be active?

## Slide 32: Data path for Branch-on-Equal Instruction
For example, beq $t1, $t2, offset
Four steps:
  An instruction fetched and the PC incremented.
  Two registers, $t1 and $t2, read from the register file.
  The ALU performs a subtract on the data values read from the register file. Also, the value of PC + 4 is added to the sign-extended, lower 16 bits of the instruction shifted left by two; the result is the branch target address.
  The Zero result from the ALU is used to decide which adder result to store into the PC.

## Slide 33
Which control lines should be active?

## Slide 34: Review question
Fill in the table below.
Instruction | RegDst | ALUSrc | Memto- Reg | Reg- Write | Mem- Read | Mem- Write | Branch | ALUOp1 | ALUOp0
R-format |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 

## Slide 35: Review question
Design the digital logic circuit for the main control unit.

## Slide 36: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
Pipelining can improve performance.

## Slide 37: Conclusions
We have implemented R-format, store/load, and bne MIPS instructions using a single clock cycle.
  The main control unit
  The ALU control unit
  The ALU unit
  Two adders
  The memory (instruction and data)
  Register file
  4 MUXes
  Sign extend
  Bit shifter
  AND gate
  PC

## Slide 38: Reading
Read B.7-B.8 in David Patterson and John Hennessy, Computer Organization and Design, 5th edition, Morgan Kaufmann, 2014.

## Slide 39: Acknowledgements
This set of slides are prepared mainly based on
  The slides prepared by K. Asanovic & V. Stojanovic for CS61C at UC/Berkeley (http://inst.eecs.Berkeley.edu/~cs61c/sp15)