## Slide 1: 8. Cache
Rocky K. C. Chang
27 November 2017

## Slide 2: Goals of this lecture
Understand the tradeoff among size, cost and performance of NRAM, DRAM, Flash and secondary storages.
Understand the two principles of locality: temporal and spatial.
Understand how cache provides the illusion of accessing a fast and vast memory.
Understand the Direct Mapped, Set Associativity and Fully Associative methods to find block in cache using Tag field and Valid bit for Hit.
Understand how Write-Through vs. Write-Back support the memory store operations.

## Slide 3: The memory hierarchy

## Slide 4: Semiconductor memories
Source: https://github.com/PatternAgents/Electronics_One_Workshop/wiki/Memory-Circuits

## Slide 5: memory performance and cost

## Slide 6: SRAM vs DRAM

## Slide 7: Processor-DRAM Gap (latency)
Time
µProc 60%/year
DRAM
7%/year
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (growing 50%/yr)
Performance
1980 microprocessor executes ~one instruction in same time as DRAM access
2015 microprocessor executes ~1000 instructions in same time as DRAM access

## Slide 8: Big Idea: Memory Hierarchy
Processor
Size of memory at each level
Increasing distance from processor, decreasing speed
Level 1
Level 2
Level n
Level 3
. . .
Inner
Outer
Levels in memory hierarchy
As we move to outer levels the latency goes up and price per bit goes down. Why?

## Slide 9: A Library Analogy
Writing a report based on books on reserve.
  E.g., works of Shakespeare
Go to library to get reserved book and place on desk in library.
If need more, check them out and keep on desk.
  But don’t return earlier books since might need them
You hope this collection of ~10 books on desk enough to write report, despite 10 being only a small percent of all the books in a library.

## Slide 10: Real Memory Reference Patterns
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)

## Slide 11: Big Idea: Locality
Temporal Locality (locality in time)
  Go back to the same book on desktop multiple times.
  If a memory location is referenced, then it will tend to be referenced again soon.
Spatial Locality (locality in space)
  When go to book shelf, pick up multiple books by Shakespeare since library stores related books together.
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon.

## Slide 12
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)
Spatial
Locality
Temporal
Locality

## Slide 13: Principle of Locality
Principle of Locality: Programs access small portion of address space at any instant of time.
What program structures lead to temporal and spatial locality in instruction accesses?
In data accesses?

## Slide 14: Memory Reference Patterns
Address
Time
Instruction
fetches
Stack
accesses
Data
accesses
n loop iterations
subroutine call
subroutine return
argument access
vector access
scalar accesses

## Slide 15: Cache Philosophy
Programmer-invisible hardware mechanism to give illusion of speed of fastest memory with size of largest memory.
  Works fine even if programmer has no idea what a cache is.
  However, performance-oriented programmers today sometimes “reverse engineer” cache design to design data structures to match cache.

## Slide 16: Memory Access without Cache
Load word instruction: lw $t0,0($t1)
$t1 contains 1022ten, Memory[1022] = 99
  Processor issues address 1022ten to memory
  Memory reads word at address 1022ten (99)
  Memory sends 99 to processor
  Processor loads 99 into register $t0

## Slide 17: Adding Cache to Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache
Source: Slides by K. Asanovic & V. Stojanovic for CS61C at UC/Berlekey

## Slide 18: Memory Access with Cache
Load word instruction: lw $t0,0($t1)
$t1 contains 1022ten, Memory[1022] = 99
With cache (similar to a hash)
  Processor issues address 1022ten to cache.
  Cache checks to see if has copy of data at address 1022ten.
    2a. If finds a match (Hit): cache reads 99, sends to processor.
    2b. No match (Miss): cache sends address 1022 to memory
      Memory reads 99 at address 1022ten.
      Memory sends 99 to cache.
      Cache replaces word with new 99.
      Cache sends 99 to processor.
  Processor loads 99 into register $t0.

## Slide 19: Cache “Tags”
Need way to tell if have copy of location in memory so that can decide on hit or miss.
On cache miss, put memory address of block in “tag address” of cache block.
  1022 placed in tag next to data from memory (99)
Tag | Data
252 | 12
1022 | 99
131 | 7
2041 | 20
From earlier
instructions

## Slide 20: Anatomy of a 16 Byte Cache, 4 Byte Block
Operations:
  Cache Hit
  Cache Miss
  Refill cache from memory
Cache needs Address Tags to decide if Processor Address is a Cache Hit or Cache Miss
  Compares all 4 tags
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041

## Slide 21: Cache Replacement
Tag | Data
252 | 12
1022 | 99
131 | 7
2041 | 20
Tag | Data
252 | 12
1022 | 99
511 | 11
2041 | 20
Suppose processor now requests location 511, which contains 11.
Doesn’t match any cache block, so must “evict” one resident block to make room.
  Which block to evict?
Replace “victim” with new memory block at address 511.

## Slide 22: Cache Terms
Hit rate: fraction of accesses that hit in the cache
Miss rate: 1 – Hit rate
Miss penalty: time to replace a block from lower level in memory hierarchy to cache
Hit time: time to access cache memory (including tag comparison)

## Slide 23: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses in the cache.
AMAT = Time for a hit + Miss rate x Miss penalty
  Time for a hit = hit detection + data transfer
  Miss penalty = the time required to fetch the block from the next lower level of the hierarchy and load it into the cache.
Example:
A processor with a 1 ns clock cycle time
A miss penalty of 20 clock cycles
A miss rate of 0.05 misses per instruction
A cache access time (including hit detection) of 1 clock cycle.
AMAT = 1 + 0.05 × 20 = 2 clock cycles (i.e., 2 ns)

## Slide 24: Block Must be Aligned in Memory
Word blocks are aligned, so binary address of all words in cache always ends in 00two.
  Word alignment: data are stored at an address that is divisible by 4.
Don’t need to compare last 2 bits of 32-bit byte address (comparator can be narrower)
=> Don’t need to store last 2 bits of 32-bit byte address in Cache Tag (Tag can be narrower)

## Slide 25: Anatomy of a 32B Cache, 8B Block
Blocks must be aligned in pairs, otherwise could get same word twice in cache
Tags only have even-numbered words
Last 3 bits of address always 000two
Tags, comparators can be narrower
Can get hit for either word in block
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
42
1947
12
130
2040
1000
7
20
-10

## Slide 26: Hardware Cost of Cache
Need to compare every tag to the Processor address.
Comparators are expensive.
Optimization: 2 sets => ½ comparators
1 address bit selects which set.
26
Processor
32-bit
Address
Tag
Data
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
Tag
Data
Set 0
Set 1

## Slide 27: Processor Address Fields used by Cache Controller
Block Offset: Byte address within block
Set Index: Selects which set
Tag: Remaining portion of processor address
Size of Index = log2 (number of sets)
Size of Tag = Address size – size of Index – log2 (number of bytes per block)
Block offset
Set Index
Tag
Processor Address (32-bits total)

## Slide 28: limit to number of sets
Can save more comparators if have more than 2 sets.
Limit: As many sets as cache blocks – only needs one comparator!
  This is called “Direct-Mapped” Design
Block offset
Index
Tag

## Slide 29
Source: Stallings, Computer organization and architecture: Designing for performance, 9th edition, Prentice Hall, 2013.

## Slide 30: Mapping a 6-bit Memory Address 1/2
Block size is 4 bytes (1 word). It could be multi-word.
Memory and cache blocks are of the same size, unit of transfer between memory and cache
# Memory blocks >> # Cache blocks
  16 Memory blocks/16 words/64 bytes/6 bits to address all bytes
  4 cache blocks, 4 bytes (1 word) per block
  4 memory blocks map to each cache block
0
5
1
Byte Offset Within Block (e.g., 1 word)
2
3
Block within cache
Index
4
Mem Block within cache Block
Tag

## Slide 31: Mapping a 6-bit Memory Address 2/2
Byte within block: low order two bits, ignore! (nothing smaller than a block)
Memory block to cache block, aka index: middle two bits
Which memory block is in a given cache block, aka tag: top two bits
0
5
1
Byte Offset Within Block (e.g., Word)
2
3
Block within cache
Index
4
Mem Block within cache Block
Tag

## Slide 32: One More Detail: Valid Bit
When start a new program, cache does not have valid information for this program.
Need an indicator whether this tag entry is valid for this program.
Add a “valid bit” to the cache tag entry.
  0 => cache miss, even if by chance, address = tag
  1 => cache hit, if processor address = tag

## Slide 33: Caching: A Simple First Example
00
01
10
11
Cache
Main Memory
Q: Where in the cache is the mem block?
Use next 2 low-order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q: Is the memory block in cache?
Compare the cache tag to the high-order 2 memory address bits to tell if the memory block is in the cache (provided valid bit is set)
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits (xx) define the byte in the block (32b words)
Index

## Slide 34: Direct-Mapped Cache Example
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Block offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator
One word blocks, cache size = 1K words (or 4KB)

## Slide 35: Multiword-Block Direct-Mapped Cache
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
What kind of locality are we taking advantage of?
Four words/block, cache size = 1K words

## Slide 36: Example: Direct-Mapped cache with 4 Single-Word Lines
Consider the main memory address reference string
  0 4 0 4 0 4 0 4
0
4
0
4
0
4
0
4
Start with an empty cache - all blocks initially marked as not valid

## Slide 37: Example: Direct-Mapped cache with 4 Single-Word Lines
0
4
0
4
0
4
0
4
miss
miss
miss
miss
miss
miss
miss
miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
00 Mem(0)
01
4
00 Mem(0)
01
4
00 Mem(0)
01
4
01 Mem(4)
0
00
01 Mem(4)
0
00
Start with an empty cache - all blocks initially marked as not valid
Ping-pong effect due to conflict misses - two memory locations that map into the same cache block
  8 requests, 8 misses

## Slide 38: Alternative Block Placement Schemes 1/2
Direct mapped placement: mem block 12 in 8 block cache: only one cache block where mem block 12 can be found—(12 modulo 8) = 4.
Set associative placement: four sets × 2-ways (8 cache blocks), memory block 12 in set (12 mod 4) = 0; either element of the set.
Full associative placement: mem block 12 can appear in any cache blocks.

## Slide 39: Alternative Block Placement Schemes 2/2
“Fully Associative”: Block can go anywhere
  First design on slide 19
  Note: No Index field, but 1 comparator/block
“Direct Mapped”: Block goes to one place
  Note: Only 1 comparator
  Number of sets = number blocks
“N-way Set Associative”: N places for a block
  Number of sets = number of blocks / N
  Fully Associative: N = number of blocks
  Direct Mapped: N = 1

## Slide 40: Example: 2-Way Set Associative cache (4 words = 2 sets x 2 ways per set)
0
Cache
Main Memory
Q: How do we find it?
Use next 1 low order memory address bit to determine which cache set (i.e., modulo the number of sets in the cache)
Tag
Data
Q: Is it there?
Compare all the cache tags in the set to the high order 3 memory address bits to tell if the memory block is in the cache
V
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Set
1
0
1
Way
0
1
One word blocks
Two low order bits define the byte in the word (32b words)
Notes: This picture is as opposed to
Way 0
both red Set 0
Way 1
------------------------------------
Way 0
both green Set 1
Way 1

## Slide 41: Example: 4-Word 2-Way SA cache
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
0
4
0
4
Start with an empty cache - all blocks initially marked as not valid

## Slide 42: Example: 4-Word 2-Way SA cache
0
4
0
4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Start with an empty cache - all blocks initially marked as not valid
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Solves the ping-pong effect in a direct-mapped cache due to conflict misses since now two memory locations that map into the same cache set can co-exist!
  8 requests, 2 misses
Notes: Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 43: Different Organizations of an Eight-Block Cache
Total size of cache in blocks = number of sets × associativity.
For a fixed cache size, increasing associativity decreases number of sets while increasing number of elements per set.
With eight blocks, an 8-way set-associative cache is same as a fully associative cache.

## Slide 44: Four-Way Set-Associative Cache
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3

## Slide 45: Range of Set-Associative Caches
For a fixed-size cache, each increase by a factor of 2 in associativity doubles the number of blocks per set (i.e., the number of “ways”) and halves the number of sets –
  decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Index
Tag
More Associativity (more ways)

## Slide 46: Costs of Set-Associative Caches
N-way set-associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision). DM cache: block is available before the Hit/Miss decision
    In Set-Associative, not possible to just assume a hit and continue and recover later if it was a miss
When miss occurs, which way’s block selected for replacement?
  Least Recently Used (LRU): one that has been unused the longest (principle of temporal locality)
    Must track when each way’s block was used relative to other blocks in the set
    For 2-way SA cache, one bit per set → set to 1 when a block is referenced; reset the other way’s bit (i.e., “last used”)

## Slide 47: Cache Replacement Policies
Random Replacement
  Hardware randomly selects a cache evict
Least-Recently Used
  Hardware keeps track of access history
  Replace the entry that has not been used for the longest time
  For 2-way set-associative cache, need one bit for LRU replacement
Example of a Simple “Pseudo” LRU Implementation
  Assume 64 Fully Associative entries
  Hardware replacement pointer points to one cache entry
  Whenever access is made to the entry the pointer points to:
    Move the pointer to the next entry
  Otherwise: do not move the pointer
  (example of “not-most-recently used” replacement policy)
:
Entry 0
Entry 1
Entry 63
Replacement
Pointer

## Slide 48: Benefits of Set-Associative Caches
Choice of DM cache or SA cache depends on the cost of a miss versus the cost of implementation.
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate).

## Slide 49: Typical Memory Hierarchy
Second-Level
Cache
(SRAM)
Principle of locality + memory hierarchy presents programmer with ≈ as much memory as is available in the cheapest technology at the ≈ speed offered by the fastest technology.
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Cost/bit: highest lowest
Third-Level
Cache
(SRAM)

## Slide 50: Handling Stores with Write-Through
Store instructions write to memory, changing values
Need to make sure cache and memory have same values on writes: 2 policies
1) Write-Through Policy: (a) write cache and (b) write through the cache to memory
  Every write eventually gets to memory.
  Too slow, so include a Write Buffer to allow processor to continue once data in the Buffer.
  Buffer updates memory in parallel to processor.

## Slide 51: Write-Through Cache
Write both values in cache and in memory.
Write buffer stops CPU from stalling if memory cannot keep up.
Write buffer may have multiple entries to absorb bursts of writes.
What if store misses in cache?
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041
Addr
Data
Write Buffer

## Slide 52: Handling Stores with Write-Back
2) Write-Back Policy: write only to cache and then write cache block back to memory when it is evicted from the cache.
  Writes collected in cache, only single write to memory per block.
  Include a bit to see if wrote to block or not, and then only write back if bit is set
    Called “dirty” bit (writing makes it “dirty”)

## Slide 53: Write-Back Cache
Store/cache hit, write data in cache only and set dirty bit
  Memory has stale value
Store/cache miss, read data from memory, then update and set dirty bit
  “Write-allocate” policy
Load/cache hit, use value from cache
On any miss, write back evicted block, only if dirty. Update cache with new block and clear dirty bit.
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041
D
D
D
D
Dirty Bits

## Slide 54
https://en.wikipedia.org/wiki/Cache_(computing)

## Slide 55: Write-Through vs. Write-Back
Write-Through:
  Simpler control logic
  More predictable timing simplifies processor control logic
  Easier to make reliable, since memory always has copy of data (big idea: Redundancy!)
Write-Back
  More complex control logic
  More variable timing (0,1,2 memory accesses per cache access)
  Usually reduces write traffic
  Harder to make reliable, sometimes cache has only copy of data.

## Slide 56: Conclusions
Principle of Locality for Libraries /Computer Memory
Hierarchy of memories (speed/size/cost per bit) to exploit locality
Cache – copy of data at the lower level in memory hierarchy
Direct Mapped, Set Associative and Fully Associative to find block in cache using Tag field and Valid bit for Hit
Cache design choice:
  Write-Through vs. Write-Back

## Slide 57: Reading
Read 5.1-5.3 in David Patterson and John Hennessy, Computer Organization and Design, 5th edition, Morgan Kaufmann, 2014.

## Slide 58: Acknowledgements
This set of slides are prepared largely based on
  The slides prepared by K. Asanovic & V. Stojanovic for CS61C at UC/Berkeley (http://inst.eecs.Berkeley.edu/~cs61c/sp15)